## Slide 1: Managed Wi-Fi UNMS
Ruckus Access Point Solution Document

## Slide 2: Introduction
The purpose of this document is to provide a comprehensive overview of our API-based data collection and reporting initiative. Specifically, we aim to detail the processes involved in collecting data related to "Inventory Details," "Performance KPIs," and "Alarms" in Ruckus Access Points (APs). Through this document, you will gain insights into the methodologies employed, the tools and technologies leveraged, and the resulting data visualizations/UNMS Dashboarding.
Ruckus offers a range of Wi-Fi devices deployed within Airtel for managed Wi-Fi services, including the following:
Ruckus R350
Ruckus R550
Ruckus R650
Ruckus R750
Ruckus T350c
Unleashed T750
These devices are part of the Ruckus family and contribute to the robust managed Wi-Fi infrastructure provided by Airtel.

## Slide 3: M-Wifi UNMS Modules and Solution Use-cases
AAA Server Module
24Online
NAS Box Module
24Online
Access Point Module
Ruckus
L2-Switch Module
D-Link
Network Stitching Module
Correlation and Alerting
Module
APIs based collection
Inventory details
Performance KPIs
API Alarms
Live Node Reachability Checker Module
API/SNMP based Data collection
User usage
Authentication(SMS) Data
SNMP based Traps
Lab testing of
SNMP based collection switches ~1500 Devices
All NAS Box configuration details
API/SNMP based collection
NAS Box configuration details (Read Only)
SNMP based Traps
Identification of connectivity between different network components
Relationship establishment
Correlation with performance and alarms
Custom Queue
Alarm compression
Providing Alarms /events as per custom requirements
ICMP/API Based availability for AAA Server/NAS Box
ICMP/API Based availability for Access Point
ICMP/SNMP bases availability for L2 switches
Total Timeline : 20 Weeks
**Note : ALL Modules are for Read Only Actions and will not support any write back or change actions

## Slide 4: Process for Module(s) Delivery
Requirement gathering
Requirement Signoff**
Development, Testing/Validation
Scaling up and Q&A
Handing over to Airtel
UAT
** The Current provided LOE is based on the current requirements. If the requirements changes the LOE might be impacted or the new requirements will be taken up as a separate new task
For Each of the Modules following Development cycle will be followed
Requirement Gathering : CEMTics will understand the requirements from Airtel and create a solution document which will contain the Proposed solution or Proposed Report format along with tentative timelines and development priority
Requirement SIgnoff : The solution document will be presented to Airtel and Airtel has to provide a go ahead for the solution creation. The solution will only be created once Airtel provides a go ahead. Once the requirements are frozen any further modification will be treated as a separate Task
Development, Testing/Validation : CEMtics will Develop the code and will Internally test and validate the results. The initial Limited output will also be shared with Airtel for their information and records
Scaling up and Q&A : Post Initial testing and development the code will be rolled out for the entire range of devices
Handing over to Airtel : The Final rollout info will be shared with Airtel and only the BUGs arising if any from the delivered module will be fixed. Any new report or new requirement will be considered as a separate task and will be budgeted separately and will be taken over for development as per available backlog .
UAT : UAT needs to be completed within 7-10 days after the module is delivered and handed over to Airtel
All the existing and new requirements will follow the above defined process and life cycle

## Slide 5
API Details –
Supported API Versions:
The provided API supports the following version, each denoted by a specific version number. The supported API versions are as follows:
1. v8_0
2. v8_2
3. v9_1
API for Data Collection:
API | Granularity
{{ _.url }}/v9_1/ap | 24 Hrs
{{ _.url }}/v9_1/rkszones | 24 Hrs
{{ _.url }}/v9_1/rkszones/zone_id/apgroups | 24 Hrs
{{ _.url }}/v9_1/aps/{apMac} | 24 Hrs
{{ _.url }}/v9_1/aps/{apMac}/operational/summary | 3 Min
{{ _.url }}/v9_1/rkszones/zone_id/wlans | 24 Hrs
{{ _.url }}/v8_0/aps/{apMac}/operational/alarms | 3 Min
{{ _.url }}/v8_2/aps/{apMac}/operational/client | 3 Min
{{ _.url }}/v9_1/rkszones/{zoneid}/wlans/{wlanid} | 24 Hrs
{{ _.url }}/v9_1/rkszones/{zoneid}/wlans | 24 Hrs

## Slide 6: Login Details
Logon Session Credential:
To access and interact with the API, you need to provide logon session credentials. These credentials are used to authenticate and verify your identity before accessing the API's data and functionality. To the provided logon session credentials include:
URL IP: “61.95.251.130”
Username: "admin"
Password: "Admin@123"
Time Zone UTC Offset: "+05:30“
**However, we will be required Service Ticket for data collection via python
Python code for api data collection-

## Slide 7: Ruckus AP APIs Hierarchy
Zones
AP Groups
WLANs
APs
AP Events
AP Alarms
AP Mac Info
Clients
AP Operation Summary

## Slide 8: Ruckus AP APIs Inventory Keys and Attributes
Get AP List
api_aplist
/v9_1/aps
AP Mac | Zone | AP Group | AP serial | AP model | AP name | AP description | AP location | AP s/w version | AP wifi24Channel | AP wifi50Channel | AP IP | NAS IP (externalIp) | NAS Port (externalPort) | AP provisionMethod | AP approvedTime (Registered ON) | AP lastSeenTime
Get Zone Info
api_zones
/v9_1/rkszones
Get AP Group Info
api_apgroups
/v9_1/rkszones/{zoneID}/apgroups
api_apopsummary
v9_1/aps/{mac}/operational/summary
api_apmac
/v9_1/aps/{mac}
api_wlans
/v9_1/rkszones/{zoneid}/wlans
Keys
Attributes
*Data to be refreshed/published every 24 hrs

## Slide 9: Inventory – Algorithm for data collection and Stitching
Start 24hr timer
Get Zone Details
Start next ROP Measurements
Inventory data data to be polled every 24 hrs.
Wait for 24hr timer completion.
Get WLAN Details
Get AP Group Details
Get Connected AP Details
Update all values in Inventory database with current ROP time
Stitch All Data with common keys

## Slide 10: Reports
AP Inventory –
Attributes | Sample Value | API | API Attribute Name
AP MAC | 10:F0:68:1E:71:E0 | {{ _.url }}/v9_1/ap | mac
AP Name | 4.041E+15 | {{ _.url }}/v9_1/ap | name
Description | 12th Floor,Inside Commercial-1 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | description
IP Address | 10.0.0.11 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | ip
Model | R510 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | model
Zone | Dr.LAL PATH LAB | {{ _.url }}/v9_1/aps | zoneId/Zone Name
AP Group | Dr.LAL PATH LAB | {{ _.url }}/v9_1/aps | apGroupId
AP Firmware | 5.2.2.0.301 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | version
Serial | 1.62202E+11 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | serial
Location | 4.041E+15 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | location
Administrative State | Unlocked | {{ _.url }}/v9_1/aps/{apMac} | administrativeState
Registration State | Approved | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | registrationState
Provision Method | Discovered | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | provisionMethod
Provision Stage | N/A | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | provisionStage
Management VLAN | 1 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | managementVlan
Mesh Role | DISABLED | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | meshRole
NAS IP:Port | 61.246.202.54:52246 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | externalIp:externalPort
Configuration Status | Up-to-date | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | configState
Channel (2.4G) | 11 (20MHz) | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | wifi24Channel
Channel (5G) | 104 (80MHz) | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | wifi50Channel

## Slide 11: Ruckus AP Performance APIs Keys and Attributes
Get AP List
api_aplist
/v9_1/aps
Get Zone Info
api_zones
/v9_1/rkszones
Get AP Group Info
api_apgroups
/v9_1/rkszones/{zoneID}/apgroups
api_apopsummary
v9_1/aps/{mac}/operational/summary
api_apmac
/v9_1/aps/{mac}
api_wlans
/v9_1/rkszones/{zoneid}/wlans
Keys
AP Performance Attributes
AP MAC | AP Zone | AP Group | Last Seen | Uptime | Status | Registered On | Alarm Count | AP RSSI | AP SNR | AP Traffic Total | AP Traffic UL | AP Traffic DL | AP Traffic 2.5G | AP Traffic 5G | AP UL Traffic 2.5G | AP UL Traffic 5G | AP DL Traffic 2.5G | AP DL Traffic 5G
Client performance Attributes and Alarms
api_apopclients
/v8_2/aps/{mac}/operational/client
api_apopevents
/v8_2/aps/{mac}/operational/events
api_alarmsummary
v9_1/aps/{mac}/operational/alarms
Aggregate/Transform Client wise data to AP wise data
*Data to be refreshed/published every 15 mins

## Slide 12: Performance - Algorithm for Traffic
Get Client data for AP for current ROP Nth interval and start 3 min timer
Sum Total UL Traffic per AP on 2.4 Ghz
Customers latched on which Band ?
Sum Total UL Traffic per AP on 5 Ghz
Sum Total Traffic per AP on 2.4 Ghz
Sum Total DL Traffic per AP on 2.4 Ghz
Sum Total Traffic per AP on 5 Ghz
Sum Total DL Traffic per AP on 5 Ghz
Sum Total Traffic per AP
Start next ROP Measurements
No
2.4 Ghz
5 Ghz
Client data to be polled every 3 mins.
Data aggregation to be done every 15 mins(ROP)
Performance data for UL/DL traffic is available band wise per client per AP.
Traffic to be evaluated separately for :
  2.4 Ghz Band
  5GHz Band
  UL and DL
Wait for 3 min timer completion.
Is N=5
No
N=N+1
Yes
N=1
Update all values in database with current ROP time

## Slide 13: Performance- Algorithm for Throughput, RSSI and SNR
Get Client data for AP for current ROP Nth interval(3min)
Average SNR of all customers for 2.4Ghz
Customers latched on which Band ?
Average SNR of all customers for 5Ghz
Start next ROP Measurements
No
2.4 Ghz
5 Ghz
Data aggregation for throughput, rssi and snr to be done every 15 mins(ROP) for the last 3 min interval data
Throughput, rssi and snr to be evaluated separately for :
  2.4 Ghz Band
  5GHz Band
Wait for 3 min timer completion.
Is N=5
No
N=N+1
Yes
N=1
Is N=5
No
Yes
Update all values in database with current ROP time
Average RSSI of all customers for 2.4Ghz
Average RSSI of all customers for 5Ghz
Average Throughput of all customers for 2.4Ghz
Average Throughput of all customers for 5Ghz

## Slide 14: Performance Aggregation Example
15 mins
Hourly
Daily
Further Aggregations
Raw API Response
Level 1 Aggregation
Level 2 Aggregation
Level 3 Aggregation

## Slide 15: Performance- Algorithm for Alarms
Get Client data for AP for current ROP Nth interval(3min)
Average SNR of all customers for 2.4Ghz
Customers latched on which Band ?
Average SNR of all customers for 5Ghz
Start next ROP Measurements
No
2.4 Ghz
5 Ghz
Data aggregation for throughput, rssi and snr to be done every 15 mins(ROP) for the last 3 min interval data
Throughput, rssi and snr to be evaluated separately for :
  2.4 Ghz Band
  5GHz Band
Wait for 3 min timer completion.
Is N=5
No
N=N+1
Yes
N=1
Is N=5
No
Yes
Update all values in database with current ROP time
Average RSSI of all customers for 2.4Ghz
Average RSSI of all customers for 5Ghz
Average Throughput of all customers for 2.4Ghz
Average Throughput of all customers for 5Ghz

## Slide 16: Reports
AP Performance-
Attributes | Sample Value | API | API Attribute Name
AP MAC | 10:F0:68:1E:71:E0 |  | 
Clients | 5 | {{ _.url }}/v8_2/aps/{apMac}/operational/client | totalCount
Last Seen | 45112.66791 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | lastSeenTime
Uptime | 1649484 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | uptime
Status | Online | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | connectionState
Registered On | 44834.01906 | {{ _.url }}/v9_1/aps/{apMac}/operational/summary | registrationState
Alarm | 0 | {{ _.url }}/v8_0/aps/apMac/operational/alarms | totalCount
AP RSSI | -45 | To be calculated From client | 
AP SNR | 46 | To be calculated From client | 
AP Traffic Total | 135571333 | To be calculated From client | 
AP Traffic UL | 44916330 | To be calculated From client | 
AP Traffic DL | 90655003 | To be calculated From client | 
AP Traffic 2.5G | 9903033 | To be calculated From client | 
AP Traffic 5G | 13816992 | To be calculated From client | 
AP UL Traffic 2.5G | 3547558 | To be calculated From client | 
AP UL Traffic 5G | 6353464 | To be calculated From client | 
AP DL Traffic 2.5G | 6355475 | To be calculated From client | 
AP DL Traffic 5G | 7463528 | To be calculated From client | 

## Slide 17: Reports
Clients Inventory and Performance-
Attributes | Sample | Reports | API | API Attribute
APMAC | 10:F0:68:33:1A:A0 (Input in api) | Inventory | {{ _.url }}/v9_1/aps | Input
Client mac | 1 | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | mac
Client IP | 10.0.183.150/:: | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | ipAddress
Client hostname | AP-AkVpSCyp5fTV | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | hostName
Client osType | Windows | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | osType
Client radioMode | b/g/n | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | radioMode
Client channel | 1 | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | channel
Client wlanId | BFVL | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | ssid
Client ssid | BFVL | Inventory | {{ _.url }}/v8_2/aps/{apMac}/operational/client | ssid
Client rssi | -41 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | rssi
Client snr | 46 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | snr
Client rxByteRate | 12 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | rxByteRate
Client txByteRate | 10 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | txByteRate
Client rxAvgByteRate | 7 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | rxAvgByteRate
Client txAvgByteRate | 12 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | txAvgByteRate
Client fromClientBytes | 73 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | fromClientBytes
Client toClientBytes | 3874 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | toClientBytes
Client fromClientPkts | 287 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | fromClientPkts
Client toClientPkts | 3984 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | toClientPkts
Client connectedSince | 1.69926E+12 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | connectedSince
Client vlan | 10 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | vlan
Client toClientDroppedPkts | 734 | Performance | {{ _.url }}/v8_2/aps/{apMac}/operational/client | toClientDroppedPkts

## Slide 18: Reports
AP Alarms-
Attributes | Sample Value | API | API Attribute Name
AP MAC | 10:F0:68:33:1A:A0 | Take from AP inventory | 
Date and Time | 05-07-2023 16:16 | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | time
Code | 303 | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | code
Alarm Type | AP disconnected | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | type
Severity | Major | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | severity
Status | Cleared | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | status
Acknowledged On |  | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | acknowledgedTime
Cleared On | 05-07-2023 16:19 | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | clearedTime
Activity | AP [4044000010730001@10:F0:68:34:0D:E0] disconnected. | {{ _.url }}/v8_0/aps/{apMac}/operational/alarms | description

## Slide 19: Aggregation Logics
Ruckus AP The detailed logics for every attributes related to inventory, performance and Alarms have been mentioned in below spreadsheet

## Slide 20: Thank You